## Slide 1: Progress toward Phase III Design of the Project 8 Experiment
Tim Wendler
Post-Doc
Notes: The alien we are trying to communicate with

## Slide 2: Direct Neutrino Mass Limit from Tritium Beta Decay
3H → 3He+ + e- + 𝜈e
n
n
p
p
n
p
𝜈e
e-
3H
3He
β-decay
electron
anti-neutrino
Beta Decay: The masses and kinetic energies of the products must add up to the mass of original nucleus
Tritium spectrum endpoint changes with finite neutrino mass
  Determine the greatest upper-bound for electron neutrino mass from the shape of the tritium beta-decay endpoint
Measuring this electron’s initial energy is a direct method of electron neutrino mass measurement
Beta Energies
Notes: CRES

## Slide 3: Cyclotron Radiation Emission Spectroscopy (CRES)
Detector Concept
Amplifier/Digitizer
antennas
New Spectroscopy Technique: Formaggio and Monreal, Phys. Rev. D 80, 051301 (R), 2009
Magnetically Trapped Electron in a cyclotron state emits K-band (26GHz) radiation in a 1 Tesla field
Trap coil
Trap coil
Grad-B Motion
26 GHz
Notes: Project 8

## Slide 4: Project 8 Collaboration – 10 Institutions
Supported by the NSF and the DOE Office of Nuclear Physics
Notes: Phases

## Slide 5: Project 8 Long Term Logistics
Currently Running
Currently Designing
Currently Designing
 | Timeline | Scientific Goal | Source | R&D Milestone
Phase I | 2010-2016 | Proof of Principle; Kr spectrum | 83mKr | Single Electron Detection
Phase II | 2016-2019 | T-He Mass Difference (Kurie plot) m𝜈 ≲ 10-100 eV | T2 | Tritium cell systematic studies (B-field calibration)
Phase III | 2017-2022 | m𝜈 ≲ 2 eV (competitive limits) | T2 | large volume new receiver design (not waveguide)
Phase IV | 2018+ | m𝜈 ≲ 40 meV Measure m𝜈 or determine normal hierarchy | T | Atomic T source and trap large scale (100 m3) control channel count
Completed
Notes: The detector

## Slide 6: Project 8 Detector (Phase I and II)
5
Trap
Coils
Phase II insert
Phase I insert
cell
cell
3
Trap
Coils
Phase III Insert will be much bigger
University of Washington
Notes: Larger trap

## Slide 7
Trapping Electrons in Phase III (Kassiopeia)
“bathtub trap”
Trap Coils
Background Field
Trap Coils make bathtub walls
Pitch =
e-
Phase II Trap
Background Field
Notes: video

## Slide 8
Phase I Trap with two events
Notes: Here is a simulation of phase 1 bathtub Trap configuration.
There is a background 1 Tesla field over this whole space. The green loops are coils with current to generate a local field to trap the axial moving beta decays.
Shown is two electrons with the same kinetic energy but slightly different initial velocity angle as they leave the beta source nucleus.
This is how we trap the electrons to measure their energy

## Slide 9
Pitch angle relative to H field
86
85
Electron Trapped Long enough to see signal
Notes: Phase I results

## Slide 10: Initial Results – Internal Conversion Lines
Energy loss
Via cyclotron
radiation
Scattering off
A residual gas
molecule
Event starting frequency
used to build spectrum
Results from Phase I
Phys. Rev. Lett. 114 , 162501 (2015)
Ashtari et. al., J. Phys. G (2017)
O(1eV) energy resolution!
…Phase II Currently Running…
Notes: Phase II results

## Slide 11: Initial Results from Phase II –
Notes: Low counts, need bigger volume

## Slide 12: Phase III Design Features
7 coils on top of background MRI 1T field
Antennas
(My Focus)
200 cc volume in blue cylinder
2 orders bigger than previous phases to increase count rate
MRI magnet in lab at UW
Size of
Phase I and II
Notes: Got this because of by NAVY exerience

## Slide 13: Basic RADAR Imaging Principles
Antenna
Area to Image
Returning signal contains 2D range profile data
Me with the dual-polarization mono-static K-band RADAR
Chirp travelling at c toward target
Convolution with original waveform produces a range profile (Pulse Compression)
Bandwidth of chirp
Minimum object distance that can be resolved is called range-resolution
Range-resolution can be obtained:
Notes: This only tells us distances in one dimension, what about Cross-range

## Slide 14: Rayleigh Criterion for Electromagnetic Apertures
RADAR System
Solutions to poor cross-range resolution:
Move closer to image
Use smaller
Make aperture bigger
Or…
Limit of Cross-Range Resolution
Limit of Cross-Range Resolution

## Slide 15: Synthesize a larger aperture
RADAR System
synthesize the aperture with the data made at different points in space
Mono-static Synthetic Aperture RADAR (SAR): Tx/Rx are at same position for each point in the phase history
Phase History
Limit of Cross-Range Resolution
Limit of Cross-Range Resolution
Area to Image

## Slide 16: Spotlight-mode Synthetic Aperture RADAR
Nearby Mountain
The Drone/Satellite stays on a perfect circular trajectory and images a single central region
More data from same area means more to be integrated out of the noise floor
Can image landscapes at night and/or through the clouds
Can only make 2D images
Bi-static SAR: Tx/Rx are at different positions
2D SAR Image without ground projection of phase history

## Slide 17: Interferometric Spotlight-mode SAR (InSAR)
Similar trajectories at multiple altitudes can produce data that can reconstruct the height of targets as well as their positions
I got my post-doc position designing Phase III because of my RADAR Imaging and microwave engineering experience.
Notes: Phase III antenna array

## Slide 18: Phase III Simulation of Antenna Array
Surface currents generated
Electric Field
Magnitude Shown
Shown is a trapped electron radiating into a surrounding antenna array
18.6keV of initial energy (Tritium Endpoint)
.9583 Tesla field
90 degree pitch
1.1 fW of power
Rectangular patch arrays couple to the field to record the signal and measure the frequency
Software: HFSS (High Frequency Structure Simulator)
Notes: Combine power in software/hardware to get out of noise floor

## Slide 19: Two Spatial Power Combining Designs (hardware)
Slotted Wave-guide Array
Lower loss in power combiner
Lower gain per element
Center Fed Series Patch Array
Higher gain per element
Higher loss in power combiner
Notes: Beam forming

## Slide 20: Software Power Combining is used to identify/isolate simultaneous events
Trapped electron off-center (Receive mode)
Beam forming to increase sensitivity to that point (Transmit mode)
Software: HFSS (High Frequency Structure Simulator)
E-field Magnitudes Shown
E-field Magnitudes Shown
Notes: Stuck in frequency domain

## Slide 21: Frequency Domain is only so useful for Phase III
Traditional Antenna Engineering is mostly in the Frequency Domain so most methods and software are optimized for frequency domain (steady-state) solutions but…
Frequency Domain is very limited
Can’t model axial motion of our source and/or the modulation that comes with it
Can only produce steady-state FEM solutions for single frequencies
Can only calculate coupling to pitch=90 time-avg electrons
Cannot use current Project 9 software to model the ADC and DAQ.
How can we model our detector in the time-domain with only frequency domain solutions?
Notes: How can we go to time-domain using powerful commercial software?

## Slide 22: Finite Impulse Response Filters
Calculate transfer function of antenna in frequency domain
Use IFFT of transfer function to generate an impulse response
Impulse Response can be used in time-domain to model the antenna’s amplitude and phase response to any arbitrary time-varying electromagnetic field
Locust is Project 8’s simulation package
Penny Slocum, Arina B. Telles, and Pranava T. Surukuchi use a variety of Finite Impulse Response filters in Locust, originally derived by HFSS
Transient responses of antennas to Gaussian pulse
Notes: Locust localizes

## Slide 23: Locust simulates the full Phase III detector
Penny Slocum has found a way to beam-form and localize electrons in the time-domain
y(m)
Notes: But there’s motion

## Slide 24: Locust simulates the motion and tracking
Penny Slocum has found a way to beam-form and track electrons in the time-domain
Phases of each array must be shifted to match CRES
Notes: At this point, Need for lab measurement calibration

## Slide 25: Locust simulates antennas in Transmit and Receive modes
Pranava has added an ideal magnetic dipole in Locust
This will allow us to normalize Locust with lab measurements
Generates an over-simplified version of CRES field
antennas
Notes: Challenges of free-field

## Slide 26: Challenges of Phase III
linear
Elliptical
CRES Free-fields contain complicated polarizations and time-dependence that is very hard to couple to linearly polarized structures
Motion produces Doppler modulation and Amplitude modulation
Currents on metal
Electric Field Phasors Shown
Notes: Is there a way to R&D in the lab?

## Slide 27: Synthesizing CRES Antenna for Array Tests
Can we make an antenna that can simulate the radiation off a single electron in a cyclotron state?
E-field Magnitudes in space surrounding CRES

## Slide 28: Yes: Turnstile Antenna
Generates full field
Requires 4 single-ended signals
Ferrous Tubes enhance magnetic dipole radiative moment
2-differential modes, in quadrature
Turnstile
CRES
Volts
Volts

## Slide 29: Synthetic CRES Antenna for Array Tests
Turnstile is essentially a mono-pole moment spinning around at 26 GHz
Current Design for fabrication

## Slide 30: The point
Good Coupling over max amount of pitch angles
Good detection volume
High count rate
High statistics
High mass sensitivity

## Slide 31: Summary
Phase I and II have demonstrated CRES in a small volume
Phase III is CRES in a large volume and the free-fields are challenging to couple to with conventional antenna engineering
Locust is a powerful simulation package that is aiding us in the design of phase III
Locust now has Antennas FIR filters for transmit and receive
Synthtic CRES Transmitter will aid in the array design and Locust calibration

## Slide 32: The End
Thank You Luiz, Penny, Mark, Maurio, and Brent